# Multi-Engine Piston Aeroplane Endorsement

General Aircraft Data

1.

a)	What is the make, type and model of the Aeroplane?

PIPER PA23-250 Aztec “C”;

b)	In which category (categories) is the aeroplane permitted to fly?

VFR, Night VFR, IFR;

Airspeed Limitation

2.

a)	List the applicable airspeeds for the aeroplane type:

Vno = 175 Kt

Vmax x/w = 20 Kt

Va = 131 Kt

Vx = 93 Kt

Turbulence penetration speed = 131 Kt

Yy = 104 Kt

Vfe – first extension = 141 Kt

Vfe > first extension = 123 Kt (25°); 109 Kt (50°)

Vlo1 = 132 Kt

Vle = 132 Kt

Vlo2 = 132 Kt

Vne= 221 Kt

b)	maximum landing light operating speed:

N/A

c)	maximum load factor (flaps up):

???

d)	maximum load factor (flaps down) is:

???

Emergency Procedures

3.	Detail the emergency procedures for the following situations:

a)	engine fire on the ground

UNSPECIFIED IN HANDLING NOTES

Mixture IDLE CUT-OFF

Throttle OPEN

Crank engine

if started, continue running to pull the fire into the engine

if not extinguished

Fuel OFF

Mixture Idle Cut-off

externally extinguish fire

b)	engine failure after take-off

UNSPECIFIED IN HANDLING NOTES

Below ??? Kt and gear Down

Abort take-off

Throttles CLOSE

Land straight ahead

Maximum braking

Master OFF

Fuel OFF

Above ??? Kt and not enough runway remaining:

Pitch UP

Power UP

Gear UP if insufficient altitude to reach airport with gear extended (using hand pump if left engine has failed (30-40 strokes)

Flap UP (using hand pump if left engine has failed (12 strokes)

Dead foot, Dead Engine

Retard throttle on dead engine to confirm

Best climb speed 89 Kt

Trim

Secure engine: (do we identify/feather dead engine before gear and flap raised???)

Prop FEATHER (full aft)

Mixture Idle Cutoff

3( bank to live engine

Fuel pump OFF

Magnetos OFF

Cowl flap CLOSED

Alternator OFF

Reduce electrical load

Fuel OFF

c)	engine fire airborne

UNSPECIFIED IN HANDLING NOTES

Fuel OFF

Throttle CLOSED

Prop FEATHER

Mixture IDLE CUT-OFF

Cowl flap OPEN

d)	engine failure in the cruise

Power UP

Maintain at least 69 Kt (Vmca)

Dead Foot, Dead Engine

Retard throttle to confirm

Pitch control fully back

e)	electrical fire on the ground

f)	electrical fire in flight

g)	cabin fire in flight

h)	rapid depressurisation

N/A

i)	waste gate failure

N/A

j)	emergency undercarriage extension procedure

Select gear control down

30-40 strokes off manual hydraulic pump

If this fails, then use the Emergency Gear Extender:

Select gear control down

Pull emergency gear extender located beneath cover plate under pitlots seat

k)	optimum glide speed for the aeroplane is

???

l)	propeller overspeed

UNSPECIFIED IN HANDLING NOTES

Retard Throttle

Check OIL pressure

Propeller FULL Decrease, then set if any control available

Reduce Airspeed

Throttle as required to remain below 2575 RPM

Normal Procedures

4.	State, describe or detail:

a)	the start sequence for cold and hot starts:

COLD:

Fuel ON

Magnetos ON

Fuel pump ON

Open Throttle ½”

Mixture full RICH until fuel flow is indicated, then IDLE-CUTOFF

Engage Starter

Mixture full RICH when engine fires

Oil Pressure CHECK

Fuel pump OFF

HOT:

Fuel ON

Magnetos ON

Open Throttle ½”

Mixture Idle-Cutoff

Engage Starter

Mixture full RICH when engine fires

Oil Pressure CHECK

b)	the RPM used for checking:

i)	the feathering system

1000-1500 RPM;

ii)	minimum RPM for feathering

1000 RPM;

iii)	the ignition system

2200 RPM;

iv)	the propeller governing system

??? RPM;

v)	the carburettor heat

N/A

c)	the maximum RPM drop and RPM differential between magnetos when checking the ignition switches

125 maximum drop, 50 maximum differential;

d)	the use of cowl flaps

UNSPECIFIED IN HANDLING NOTES

Keep engine at correct operating temperature

Open in climb and on ground

Closed for descent

As required in cruise

e)	the climb power setting, IAS, and fuel flow

24" 2400 RPM, 105 Kt, 85 Lt/hr;

f)	a typical 65% power setting, IAS and fuel flow at 5000ft pressure height

22" 2300 RPM, 79 Lt/hr, 149 Kt;

g)	using the aeroplane flight manual, calculate the endurance for the aeroplane at 5000ft AMSL (ISA) with 65% power set

4.6 Hrs;

h)	how are the mixtures leaned in the cruise

In conjunction with the EGT

125° Rich of Peak for performance cruise

Peak for endurance cruise

Weight and Balance and Performance

5.

a)	Specify the correct values of:

i)	the maximum ramp weight

2358 Kg;

ii)	the maximum take-off weight

2358 Kg;

iii)	the maximum landing weight

2240 Kg

iv)	the maximum Zero fuel weight

1995 Kg

v)	the maximum number of adult persons on board

6;

vi)	the maximum baggage weight

136 Kg;

vii)	the maximum fuel which can be carried with a full load of adult passengers (80 Kg/person) and the maximum baggage weight

201 Litres;

b)

i)	Do any of the weight limitations in i) to vii) vary between categories?

ii)	If so, what are the weight limitations of each category?

iii)	The old take-off weight, CofG position, amount of fuel and the endurance problem.

iv)	Calculate the take-off distance required at maximum take-off weight, 2500ft AMSL and OAT 30°C, and the minimum landing distance at maximum landing weight

1037 metres (3400 ft) take-off distance required

461 metres (1510 ft) landing distance required

Fuel System, Fuel and Fluids

6.	State or describe:

a)	the correct grade of fuel

100/130 (100LL ?);

b)	any approved alternate fuel

c)	the location of the fuel tanks and drain points

d)	the total and usable fuel on each tank

e)	the position of the fuel tank vents

f)	whether the engines have a carburettor or fuel injection system

Fuel Injected;

g)	if applicable, describe the priming system and its use

Prime using Throttle ½” open, Fuel pump ON, Mixture full RICH until fuel flow is indicated.

h)	where the fuel boost/auxillary pumps are located

i)	are these electrical or mechanical?

Electrical;

ii)	maximum and minimum operating pressure?

iii)	when the pumps should be used

On take-off and landing and whenever the engine drive fuel pump has failed.

i)	if applicable, the fuel tank change procedure

N/A

j)	what conditions apply to tank selection for take-off and landing?

Cross-feed is NOT selected ???;

k)	when refuelling to less than full tanks, what restrictions apply and how is the fuel quantity checked?

No restrictions.

l)	if applicable, describe the cross-feed system

m)	if applicable, the minimum and normal hydraulic fluid capacity

n)	the correct grade of oil of the aeroplane

o)	the minimum oil quantity before flight

2 quarts;

p)	the maximum quantity of oil

12 quarts;

q)	the maximum, minimum and normal engine oil pressures

Maximum 100 PSI (115 PSI?)

Minimum 25 PSI (15 PSI?)

Normal range 60 PSI - 90 PSI (55 PSI - 90 PSI?)

r)	the maximum, minimum and normal engine oil temperatures

Maximum 245°F

Minimum ???

Normal 75°F - 245°F

Asymmetric Performance

7.

a)	What IAS is Vmca in the take-off configuration?

56 Kt;

b)	What effect will full flap have on Vmca?

c)	What is the fuel flow rate with one engine shutdown at 1000 ft AMSL on an ISA day?

75% power - 43 Lt/hr;

d)

i)	What is the rate of climb with one engine shutdown, propeller feathered, max AUW, 1000 ft AMSL, take-off power, undercarriage and flap retracted on an ISA day?

~ 160 ft/min;

ii)	on an ISA+20 day?

~80 ft/min;

e)	Which engine is the critical engine?

Neither;

f)	What is the single engine climb speed (Vyse)?

88 Kt;

g)	How does single engine flight affect the range of the aeroplane?

Engines and Propeller

8.

a)	What is the make/model of the engines?

Lycoming O-360;

b)	What is the power output and number of cylinders?

180 HP, 4 cylinder;

c)	What is the take-off power setting and time limit?

2700 RPM, full throttle, no time limit;

d)	What is the maximum continues power?

2700 RPM, full throttle;

e)	Are the engines supercharged or turbo-charged?

No;

f)	What is the maximum MAP permitted?

Full throttle;

g)	If turbo-charged, what:

N/A

i)	is the type of waste gate fitted (Fixed, Manual or Automatic)?

ii)	is the procedure for operating the waste gate?

iii)	prevents the engine from being overboosted?

h)	If supercharged, what:

N/A

i)	prevents the engine from being overboosted?

ii)	controls the MAP in the climb/descent?

i)	Describe the propeller governing system

Pitch controlled by oil and nitrogen pressure.

Oil pressure sends the pitch towards high RPM/unfeather.

Nitrogen pressure and a spring sends pitch to low RPM or feather and prevents overspeeding.

Governers in each engine supply engine oil through the propeller shafts to maintain constant RPM settings.

Each propeller is controlled by a propeller control lever.

j)	If the oil pressure to the propeller dome is lost, does the propeller go into coarse or fine pitch?

Coarse pitch;

Airframe

9.

a)	What type of undercarriage system (fixed, rectractable, tricycle, conventional)?

Retractable, tricycle;

b)	Which control surfaces can be trimmed?

Stabilator;

Rudder;

c)	Describe the flap actuating system

Manually operated 4 position handle located between front seats;

d)	Describe the flap indicating system

Position of flap actuating handle;

e)	What is the flap operating range?

0°, 10°, 25°, 40°;

f)	Sketch the location of all exits

Main entry/exit hatch in fuselage over right wing;

Baggage access hatch to rear of fuselage;

Emergency exit window at left of front seat

g)	Describe the location of:

i)	landing/taxy lights

Front of nose gear;

ii)	fresh air intakes

At upper rear of fuselage (or in fin);

iii)	fuel caps

Top of engine nacelles;

h)	What is the wing span of the aeroplane?

38' 6.6";

Ancillary Systems

10.

a)	What systems are hydraulically operated?

Landing gear;

Brakes;

b)	What procedures are followed when a hydraulic system failure is suspected?

Emergency Gear Extension procedure may be required.

c)	How many brake applications would be expected from a fully pressurised brake accumulator (if applicable)?

???

d)	What are the sources of electrical power?

Battery;

Alternators;

e)	What is the DC system voltage?

12 V;

f)

i)	Can external power be used?

Yes, for starting.

ii)	If so, what is the procedure?

Master OFF

ALL electrical equipment OFF

Connect terminals

Insert external power plug

Normal start

Shutdown RIGHT engine

Remove external power plug

Master ON - check Ammeter

Check Oil pressure

Restart right engine

g)	Where are the battery and external power receptacles located?

Battery - located in nose section;

External power receptacle - located lower right side of nose section;

h)	How long can the battery supply emergency power?

???

i)	Following an alternator/generator failure in flight, which non-essential services should be switched off?

j)	Which, if any, ancillary system(s) will be lost if the left engine was shut down and the propeller feathered?

Left alternator;

k)	Which, if any, ancillary system(s) will be lost if the right engine was shut down and the propeller feathered?

Right alternator;

l)	if a stall warning device is fitted, is it electrical or mechanical?

Electrical;

m)	How is the cockpit ventilated?

Fresh air outlets at each seat area and overhead.

n)	How is the cockpit heated?

Heated air is proved by a combustion heater and distributed to the air ducts at each seat.

o)	If a fuel burning heater is installed, describe the method used to turn the heater on and off and detail any limitations.

Air intake lever partially of fully opened

Heater switch set to Heater position

Heater switch to OFF to turn heater OFF

To prevent overheat switch activation:

On the ground, turn fan ON with air intake lever in OPEN position for two minutes

In the air, leave the air intake lever in OPEN position for 15 seconds

p)	What is the fuel consumption of the heater?

1.9 Lt/hr;

q)	Describe the pressurisation system (if applicable).

N/A

r)	Show the location of the following safety equipment:

i)	fire extinguisher

ii)	ELT

Right rear of fuselage;

iii)	torches

iv)	survival equipment

v)	first aid kit

Flight Instruments

11.

a)	Where are the pitot head(s), static vent(s) and any water drain points for the pitot static system located?

Pitot/static head in located under outer left wing.

Drain is located underside left of fuselage near wing?

b)	Is there a pitot heat system fitted?

Yes

c)	Is there an alternate static source fitted? - if so:

i)	Where is this located?

Alternate static source control valve is located on left side of instrument panel.

ii)	What is the purpose of this system?

When alternate static source is selected, cabin air is used as the static source

Storm window must be CLOSED

Cabin vents must be CLOSED

Cabin heat and defroster must be ON

iii)	If used, what effect does it have on the pressure instruments?

Airspeed indicator overreads

Altimeter overreads

VSI initially indicates a climb, then reads correctly

d)	Which flight instruments are operated electrically?

Turn and Balance;

e)	Which flight instruments are gyroscopically operated?

Directional Gyro and Artificial Horizon;

f)	Which instruments are operated by vacuum?

Directional Gyro and Artificial Horizon;